## Slide 1: Crunching large graphs with commodity processors
Jacob Nelson, Brandon Myers, A. H. Hunter, Preston Briggs, Luis Ceze, Carl Ebeling, Dan Grossman, Simon Kahan*, Mark Oskin
University of Washington
*also Pacific Northwest National Laboratory
http://sampa.cs.washington.edu
HotPar 2011 Berkeley, CA
Notes: system to speed up large graph processing on clusters

## Slide 2: Introduction
Graphs important for emerging applications: social networks, bioinformatics, sensor networks, semantic databases
These graphs are big! Today, billions of vertices, edges In the future, trillions of vertices, edges

## Slide 3: Some graphs have challenging structure
Some social network metrics:
  An Experimental Study of the Small World Problem, Travers and Milgram, 1969 “6 degrees of separation”
  Planetary-Scale Views on an Instant-Messaging Network Leskovec and Horvitz, 2008 Microsoft Messenger network: 180 M vertices, 1.3 B edges: Effective diameter: 7.8
  Six Degrees of Separation, Twitter Style Alex Cheng, Sysomos Inc., 2009 Twitter network: > 100 M vertices, 5.2 B edges Effective diameter: ~6

## Slide 4: Why are these graphs hard?
Too big for one machine’s memory => Distribute across cluster
Many interesting graphs have challenging structure => Difficult to partition in a balanced way => Difficult to find locality
Bottom line: Frequent high-latency inter-node communication
For some problems, partitioning and replication help

## Slide 5: One approach: Cray XMT
Large shared memory up to 128TB across 8192 processors
Latency tolerance via concurrency: Each processor supports 1024 outstanding memory requests 128 hardware threads
Simple programming model “lots of 1MHz processors”
Application sweet spot: irregular problems with little locality slow at everything else
Notes: the only downside,
beside the price,
is performance

## Slide 6: Our position
We can beat the Cray XMT
using commodity processors
at price and performance
on all problems

## Slide 7: Our goal
SoftXMT: Lightweight multithreading in software
XMT-like Performance Programming model
Commodity Processors Interconnect
(possibly including an FPGA)

## Slide 8: Outline
The SoftXMT system
Implementation
Evaluation of SoftXMT coroutine overhead
Next steps

## Slide 9: How can we beat the XMT?
core
mem
nic
network
XMT one 500MHz core
Intel Xeon six 2.66GHz cores
core
core
mem
nic
network
. . .
66 Mref/s
140 Mref/s
30 Mref/s to 110 Mref/s
275 Mref/s
26 Mref/s to 90 Mref/s
175 Mref/s
Memops 15.6 Bref/s ~32 in flight
Memops 500 Mref/s 1024 in flight
Contexts 12
Contexts 128

## Slide 10: SoftXMT system overview
Support more contexts
Support more memory concurrency

## Slide 11: SoftXMT system overview
Support more contexts
Support more memory concurrency

## Slide 12: SoftXMT programming model
Key features: - Shared global address space - Explicit concurrency with many threads - Lightweight synchronization
Address space partitioned into - Node-private - Shared global (no caching)
Concurrency exploited via cooperative multitasking - Threads yield on long latency operations
This is infrastructure for compilers to leverage

## Slide 13: Outline
The SoftXMT system
Implementation
Evaluation of SoftXMT coroutine overhead
Conclusion

## Slide 14: Implementation: Key features
Lightweight multithreading - overhead must be low enough to allow enough threads to cover network latency
Concurrency in global memory references - must support enough outstanding references to cover network latency
Low-overhead synchronization - must avoid blocking other threads

## Slide 15: Cooperative multithreading with coroutines
prefetch a
yield load a
prefetch b
yield load b
prefetch c
yield load c
prefetch d
yield load d
Coroutine 1
Coroutine 2
Coroutine 3
Coroutine 4
Core
load a
prefetch a
yield load a
issue
complete

## Slide 16: Minimizing context switch overhead
Treat context switches as function calls; save minimal state
Switch and schedule in user space - current: round-robin - future: reactivate on operation completion
Lower context switch overhead => more ref/s
Time
Work: generate remote reference
Context switch
. . .
. . .

## Slide 17: Global memory concurrency
We need hundreds of outstanding requests per processor to cover network latency
XMT: 1024 requests per processor Xeon: ~32 requests per processor
We must manage memory concurrency ourselves

## Slide 18: Exposing local memory concurrency
Break reads and writes into two operations issue: start data moving complete: block until complete
load a
store a
prefetch a
yield load a
prefetch a
yield store d -> a
Local latency tolerance
issue
issue
complete
complete

## Slide 19: The Global Memory Manager
Tracks outstanding memory requests
On requester side: - issues request over network - waits for response - wakes thread when ready
On responder side: - performs memory request - also, synchronization operations

## Slide 20: Exposing remote memory concurrency
Break reads and writes into two operations issue: start data moving complete: block until complete
load a
store a
prefetch a
yield load a
async_send( a )
yield blocking_recv( a )
prefetch a
yield store d -> a
async_send( d, a )
yield blocking_recv( a )
Local latency tolerance
Remote latency tolerance
issue
issue
complete
complete

## Slide 21: The Global Memory Manager
Tracks outstanding memory requests
On requester side: - issues request over network - waits for response - wakes thread when ready
On responder side: - performs memory request - also, synchronization operations
load a
issue_read(a)
yield complete_read(a)
issue
complete
async_send(a)
recv(a)
load a -> d
send(d, a)
on recv(a): wakeup thread
Worker thread
Local GMM
Remote GMM

## Slide 22: Software or hardware?
Software: - dedicate core(s) to managing memory - global memory operations are function calls
Hardware: - Add FPGA accelerator on coherence bus low complexity, no computation - Encode commands in address space
Notes: communicate with it using memory operations, design the protocol to ensure that these operations complete quickly

## Slide 23: Low-overhead synchronization
For the XMT’s application sweet spot, we need - atomic increment - producer-consumer
Treat all synchronization as remote reference - separate into issue and complete - run through global memory manager - GMM owns sync variable => no atomic instructions!

## Slide 24: Outline
The SoftXMT system
Implementation
Evaluation of SoftXMT coroutine overhead
Conclusion

## Slide 25: Evaluation of SoftXMT coroutine overhead
Evaluate one piece of design: Coroutine context switch overhead
Evaluate on single node Round-robin scheduling Access local DRAM Use prefetch instructions to expose memory concurrency
Is context switch overhead low enough for - single node latencies? - multi-node latencies?

## Slide 27: Experimental Setup
Dell PowerEdge R410 dual 6-core Xeon X5650 chips (Nehalem μarchitecture) 24GB of RAM
NUMA memory architecture each chip has its own integrated memory controller Memory references to other chip’s memory go over the cache-coherent QPI
Used 1GB huge pages to reduce TLB misses
Hyperthreading disabled

## Slide 28: Can we reach hardware’s max random reference rate using coroutines?
parallel for (i in 1..n) { while (not done) { list[i] = list[i]->next
}
}
parallel for (c in 1..num_cores) { while (not done) { list[1] = list[1]->next
list[2] = list[2]->next
...
list[n] = list[n]->next
} }
parallel for (i in 1..n) { while (not done) { readIssue(&list[i]->next) yield() list[i] = readComplete(&list[i]->next)
} }
ILP
Coroutines

## Slide 29: Coroutines saturate memory bandwidth with low overhead
Notes: XMT 100 Mref/s

## Slide 30: What overhead should we expect for a multi-node system?
Questions: Can we support enough concurrency to saturate a network link? Does coroutine context storage hurt us?
Force memory operations off chip: Allocate lists in second chip’s memory, access from first chip’s cores
Emulate network latency in scheduler - Assume 3µs round-trip network latency, 100M references per second - Delay rescheduling of a coroutine for that long
No actual network communication, memory concurrency still limited by hardware

## Slide 31: What overhead should we expect for a multi-node system?
Questions: Can we support enough concurrency to saturate a network link? Does coroutine context storage hurt us?
Emulate network with 3µs round-trip latency, 100M references per second - Bandwidth: reference memory in other socket - Latency: scheduler delays memory operation
(still single node: no actual network, same memory concurrency limits)

## Slide 32: Coroutines support enough concurrency to saturate network link
32
Notes: XMT 100 Mref/s

## Slide 33: When do we blow out the cache?
Extend pointer chasing benchmark to include local working set Now, for each global reference, do n local references to b bytes of data
parallel for (i in 1..n) { while (not done) { readIssue(&remoteList[i]->next) yield() remoteList[i] = readComplete(&remoteList[i]->next) for ( i in 1 to num_local_updates ) { localList->data++; localList = localList->next; }
} }

## Slide 34: When do we blow out the cache?
Extend pointer chasing benchmark to include local working set Now, for each global reference, do n local updates to b bytes of data
2
3
Time
1
Global memory
1’s Local Memory
b bytes
n updates
2’s Local Memory
3’s Local Memory
. . .

## Slide 35: We can saturate network bandwidth even with a modest working set
Working set size per coroutine
local updates per remote
Working set size per coroutine
Network rate
Notes: op point from last experiment: ~300 coroutines
We’re run this out to absurd levels
Operating point for our applications: upper left Past 32KB: blowing out L3 cache

## Slide 36: Outline
The SoftXMT system
Implementation
Evaluation of SoftXMT coroutine overhead
Conclusion

## Slide 37: Next steps
Build software Global Memory Manager
Explore commodity network limits
Investigate synchronization

## Slide 38: Related work
Multithreading to tolerate latency Hardware: Cray XMT, SMT, Alewife, Cyclops, GPUs Software: SCM, Qthreads, MAESTRO, Charm
User-level multithreading First-class User Level Threading, Capriccio
Shared memory abstraction on distributed memory Partitioned Global Address Space Languages: UPC, CAF, Chapel, X10
Graph processing on distributed memory machines Pregel, Parallel BGL, CGMLib

## Slide 39: Also in the paper
Ideas for synchronization
More details on memory manager interface
More details on evaluation

## Slide 40: Conclusion
We think we can beat Cray XMT using commodity processors at price and performance on all problems
Vision for SoftXMT project: lots of memory concurrency + lightweight multithreading + lightweight synchronization
Our multithreading library has low enough overhead to tolerate long latencies of large high-bandwidth global memory

## Slide 41
Questions?
1
Text
http://sampa.cs.washington.edu

## Slide 43: What about commodity clusters?
Map-Reduce - not a good fit for graph problems: communication is expensive
Pregel - limited programming model - for similar performance, 10x resources compared to XMT
Top entry on Graph500: BlueGene: 8192 node machine 64x nodes for 6x performance (but on a larger problem)

## Slide 44: Graph500

## Slide 45: New coroutine approach