## Slide 1: Task 15: SoftXMT
Towards a scalable multi-node system
Simon Kahan Jacob Nelson
simon.kahan@pnnl.gov nelson@cs.washington.edu

## Slide 2: Outline
Intro and SoftXMT Vision – Simon
2011Q3 Progress and Plans -- Jacob

## Slide 3: Team
UW – started 9/30/2010 – softxmt.cs.washington.edu
  Graduate Students:
    Andrew Hunter – on leave at Google [coroutine library (“green threads”)]
    Brandon Myers – architecture, FPGAs
    Jacob Nelson – systems, FPGAs
  Faculty:
    Luis Ceze – programming & reliability of multicore systems
    Carl Ebeling – FPGA technologies
    Dan Grossman – programming language implementation
    Mark Oskin – parallel architecture
Independent
  Preston Briggs (preston@cs.washington.edu)

## Slide 4: Project Shaping Activities
4
Weekly meeting at UW – notes: softxmt.cs.washington.edu
Cray’s Task 15 report: Multi-node exploration
  Preliminary XE (Gemini) performance
  Validates our continued exploration into multi-node
Blue Waters
  Have NCSA account; waiting for access this fall
Tilera
  Recruiting a postdoc to study latency tolerance
“Crunching Large Graphs with Commodity Processors”
  Students’ paper presented in HotPar May, 2011
“Jumpthreads: software multithreading for latency tolerance”
  Andrew Hunter’s Quals, in prep for PPoPP 2012
  3x speedup on graph search & treap operations; 1.4x on sqrts

## Slide 5: SoftXMT Vision
Scale up irregular apps using mass market components
What characterizes irregular apps?
  Task flow “interrupted” by unpredictable remote references and dependencies
What are their special needs?
  Sustained task throughput in the presence of synchronization and random access latencies
5

## Slide 6: How can we compete with the XMT?
6
core
mem
nic
network
XMT one 500MHz core
Intel Xeon six 2.66GHz cores
core
core
mem
nic
network
. . .
66 Mref/s
140 Mref/s
30 Mref/s to 110 Mref/s
275 Mref/s
26 Mref/s to 90 Mref/s
175 Mref/s
Memops 15.6 Bref/s ~32 in flight
Memops 500 Mref/s 1024 in flight
Contexts 12
Contexts 128

## Slide 7: SoftXMT system overview
7
Support more contexts
Support more memory concurrency

## Slide 8: Review: Lightweight threading runtime
Why multiple contexts?
  Little’s Law: 100Mref/s bandwidth * 1us latency = 100 ops in flight
Why context switch?
  100 cores idly waiting wastes power
Why a fast sequential processor?
  Amdahl’s law: 99% parallel => at most 100x speedup
Latency tolerance necessary on multiple levels
  local memory latency is still ~100ns
8

## Slide 9: Review: Lightweight threading runtime
Built coroutine library
  Low overhead context switching (“green threads”)
  Compiler transformation (“jump threads”)
Overhead is low
  Supports hundreds of threads
  Can even tolerate local memory latency
9

## Slide 10: This review: initial experiments with multi-node
UW
  Approach for software acceleration of aggregation, atomics
Cray
  Initial multi-node experiments
  Result: ~23 Mref/s per node on HPCC Random Access
10

## Slide 11: SoftXMT system overview
11
Support more memory concurrency

## Slide 12: Global memory manager
Responsibilities
  track outstanding global requests
  aggregate requests
  perform atomic operations
  assist with thread scheduling
Three stages of implementation
  Software-only: “idealized” NIC
  Software + NIC hardware
  FPGA accelerator?
12

## Slide 13: Delegate cores
Abstraction of ideal RDMA-capable network interface
  Manage concurrent references, assist with scheduling
13

## Slide 14: Delegate cores help with aggregation
Group references by node destinations amortize network overhead
Combine atomic operations
14

## Slide 15: Delegate cores help with atomic operations
Problems
  Atomic operations introduce unnecessary fences on x86
  Network interfaces support only basic atomic operations
Alternative
  Run local atomic operations on delegate core
  Analogous to an MTA memory controller
15
atomic_mark_node( &node1 );
atomic_mark_node( &node2 );
atomic_mark_node( &node3 );
Implied fences

## Slide 16: Delegate cores help with atomic operations
  Programmer marks synchronization variables
  All synchronization variables accessed through delegate Local non-sync variables accessed by workers directly
16
No atomic operations necessary
No atomic operations necessary
Caching improves hotspot performance

## Slide 17: Delegate mechanism
State: Memory descriptor
Communication: Delegate queues Single-reader Single-writer Cacheline
Behavior:
  Coroutine
  Worker core
  Delegate core
17

## Slide 18: Delegate protocol
18
No synchronizing operations!
Tradeoffs
  Send pointer? Entire descriptor?
  Receive data? Thread Id?

## Slide 19: Why not depend on the network interface?
Network card
  Basic atomic operations
  Atomic operations cause unnecessary serialization
  Message aggregation must be done in NIC
  NIC-to-local-memory bandwidth may be limited
19
Delegate core
  Extended atomic operations
  Atomic operations can be done without synchronization
  Software can also aggregate messages
  Memory bandwidth scales with multiple delegates and memory partitioning

## Slide 20: Let’s look at some numbers
What do we have now?
  Our proof-of-implementation
Where do we think we can get?
  Our GUPS-specialized delegate
  Cray benchmarks
What will Blue Waters contribute?
  Estimates based on documentation
20

## Slide 21: Current delegate results
Benchmark: Parallel list chasing
Two single-socket Xeon "nodes"
  Delegate core manages remote communication
  Network simulated through shared memory
Goal: demonstrate that delegate data flow works
  Currently zero optimization: Experiments with individual components suggest 10x more
21

## Slide 22: Delegate infrastructure works
22
4 Mref/s per “node”

## Slide 23: Delegate performance will improve
23
> 100 Mref/s
> 100 Mref/s
23 Mref/s ?

## Slide 24: Specialized delegate performance
Single-node GUPS:
Delegate specialized for doing local atomic increments
You saw this last review
24
for i in 1..field_width { a[ b[i] ]++
}
Delegated

## Slide 25: Specialized delegate performance
25
Up to 330 Mref/s

## Slide 26: Another data point: Cray’s multi-node experiments
Cray took our code and implemented
  their own lightweight context switching library
  global memory library using Gemini network interface
Benchmarks show promise
  ~23 Mref/s per node for 8-node HPCC Random Access
  65% of XMT1 performance on same benchmark, even though XMT aggregates messages and XE6 doesn’t
We believe the delegate approach can compete with this
26

## Slide 27: What about Blue Waters?
27
core
mem
nic
network
XMT one 500 MHz core
IBM Power7 eight 4 GHz cores
core
core
mem
nic
network
. . .
66 Mref/s
140 Mref/s
30 Mref/s to 110 Mref/s
~1 Gref/s
3.5 Gref/s ?
~188 Mref/s to ~1.5 Gref/s?
Memops 64 Gref/s ~64 in flight
Memops 500 Mref/s 1024 in flight
Contexts 32
Contexts 128
For 32-core node

## Slide 28: Next steps
This summer: throughput
  Improve delegate performance
  Get network working with delegate
  Explore aggregation
Fall
  Synchronization
  Initial Blue Waters exploration
28

## Slide 29: Summary
We have a plan for multi-node
  Now we’re executing that plan
Software delegate offers advantages over NIC
  Opportunity for aggregation
  Accelerate more general synchronization
Initial performance results are promising
29