## Slide 1: Task 15: SoftXMT
1
Runtime progress
Simon Kahan simon.kahan@pnnl.gov
Jacob Nelson nelson@cs.washington.edu
Mark Oskin oskin@cs.washington.edu

## Slide 2: Team
UW – started 9/30/2010 – softxmt.cs.washington.edu
  Graduate Students:
    Brandon Holt – languages, Chapel
    Andrew Hunter – on leave at Google [coroutine library (“green threads”)]
    Brandon Myers – architecture, FPGAs
    Jacob Nelson – systems, FPGAs
  Postdocs:
    <TBD> -- Tilera Runtime
  Faculty:
    Luis Ceze – programming & reliability of multicore systems
    Carl Ebeling – FPGA technologies
    Dan Grossman – programming language implementation
    Mark Oskin – parallel architecture
Independent
  Preston Briggs (preston@cs.washington.edu)

## Slide 3: Project Shaping Activities
Blue Waters
Tilera
  Still recruiting a postdoc to study latency tolerance
"Jumpthreads: software multithreading for latency tolerance”
  Andrew Hunter submitted to PPoPP 2012
Cascadia 2011 SoftXMT Presentation (Brandon Myers)
  FPGA related workshop
  Attended by Microsoft, NVIDIA, Pico, Xilinx, UW, UWisc, UBC, U Toronto, …
Chapel
  Held an all day Task 2/8/15 meeting with PNNL, UW, Cray (Brad)
    Ongoing discussions per Task 2/8 report
Lightfleet
  Contacted & met with regarding their freespace interconnect

## Slide 4: Outline
Vision
Benchmarks
Components
  Delegate performance
  Network performance with aggregation
Collaboration
  Chapel
4

## Slide 5: Vision
5

## Slide 6: SoftXMT Vision
Scale up irregular apps using mass market components
Key features:
  Lots of concurrency
  High random access rate to global memory
  Fine-grained synchronization
  Simple programming model
6

## Slide 7: System overview
Support more contexts
Support more memory concurrency
7

## Slide 8: List chasing pseudocode
Mark global data
parallel for( int i = 0; i < NUMBER_OF_LISTS; ++i ) {
global element_t * current = get_list_head( i ); while( ! current->visited ) {
if( predicate( current->data ) )
++count;
current = current->next;
}
}
8
typedef struct element { global struct element * next; global data_t data; } element_t;
global element_t lists[] = allocate_lists();
sync global int count;
_handle = issue( READ, &current->next );
yield();
current = complete( _handle );
issue( ATOMIC_INC, &current->visited );
multi_task_queue( NUMBER_OF_LISTS, &loop_body ); run_tasks();
Mark global data
Mark data accessed atomically
Mark potential concurrency

## Slide 9: Challenges
Concurrency
  Minimize context switching time
  Support lots of contexts without blowing out cache
Global Memory
  Increase effective message rate of commodity networks
  Support languages’ memory consistency models
Synchronization
  High-throughput, avoid unnecessary serialization
  Support extended memory semantics
9

## Slide 10: Benchmarks
10

## Slide 11: What drives design
Metrics clarify what we care about:
  “if you can measure it, you can manage it”™
We care about scaling irregular threaded applications
  each concurrent subtask makes random dependent references to global memory
    metric: throughput chasing linked-lists
  work per subtask is unpredictable
    metric: throughput traversing imbalanced binary tree

## Slide 12: Imbalanced Binary Tree recursive definition for size S > 1, fixed imbalance D > 1
D==2 => balanced binary tree.
larger D => tree more imbalanced.
Choose blue or red based on result of a fair coin toss.
((S-1)/D) | 0x1
S - (((S-1)/D) | 0x1) - 1
1

## Slide 13: Example: S=14, D=3

## Slide 14: Tree Traverse: what it measures…
void Traverse(TreeNode * root) {
if (root) { future void done$; future done$ (root) { Traverse (root -> left); } Traverse (root -> right); touch (& done$); }
}
Fine-grained task expression: Making parallel work available
Producer-consumer synchronization:
Blocking, unblocking, and restarting
Fine-grained task instantiation: Finding, claiming, and beginning work

## Slide 15: Tree Traverse: … and why we care.
Captures the foundations for implementing most forms of irregular parallelism:
  Recursion
    Every irregular divide & conquer algorithm
  Loops
    On a large, non-uniform system we need dynamic scheduling to get good load balance
      divide and conquer the iteration space, ideally respecting locality where possible a la Cilk or loop future.
  Nested parallelism
    Nested loops or function calls also require dynamic scheduling
  Dataflow
    Producer-consumer synchronization

## Slide 16: Cray XMT Performance Nodes per second vs Imbalance for S=200M, D=2..128 on 4-128 processors
4
8
16
32
64
128

## Slide 17: Our goal
Beat the per node performance on Tree Traverse of Cray XMT as we scale up.
  This will indicate we have a runtime system that is at least as capable and scalable across all forms of irregular parallelism.

## Slide 18: Benchmark Zoo
Microbenchmarks (worst case performance)
  List chasing
  Imbalanced tree traversal
Applications (common case performance)
  Betweenness centrality (Brandes’ algorithm)
    Multiple nodes with aggregation
    Coarse- and fine-grained tasks
    Block transfers as well as word requests
  More to come
18

## Slide 19: Components
19

## Slide 20: SoftXMT runtime components

## Slide 21: Global memory manager
Responsibilities
  track outstanding global requests
  aggregate requests
  perform atomic operations
  assist with thread scheduling
Three stages of implementation
  Software-only: “idealized” NIC
  Software + NIC hardware
  FPGA accelerator?

## Slide 22: Delegate cores
Abstraction of ideal RDMA-capable network interface
  Accelerates atomic accesses, allows for aggregation

## Slide 23: Delegate performance experiments
Experiment setup:
  List chasing on 5 cores
  All requests go through delegate on 6th core
  Requests sent to delegate in batches
Previous results
  ~5 million requests per second through delegate
Goals
  More than network card’s limit of 20 Mreq/s
  Near single-core DRAM limit of ~100 Mreq/s

## Slide 24: Delegate performance is no longer a bottleneck
Faster than network interface

## Slide 25: Exploring network performance
Two hardware vendors
  Mellanox ConnectX-2 40Gbit Infiniband
    Thanks to HPC Advisory Council for access
    “off-load” architecture
    “Verbs” API
  QLogic TrueScale 40Gbit Infiniband
    “on-load” architecture
    “PSM” API
GASNet for job setup/teardown

## Slide 26: Measuring raw network performance
Experiment setup:
  List chasing on two nodes
  One node chases lists in other node’s memory
Goal
  Approach peak network card performance: ~20 Mreq/s per node

## Slide 27: Raw message rate

## Slide 28: Measuring aggregation performance
Experiment setup:
  List chasing on two nodes
  One node chases lists in other node’s memory
  Requests are delayed to form an aggregate message
Goal
  Approach bandwidth-saturating message rate: ~250 Mreq/s per node

## Slide 29: Aggregate message rate

## Slide 30: Next steps
Lots of challenges in getting good performance with these cards
Multi-threaded performance is unsupported/unreliable; Multi-process nodes complicate language support
All these rates are lower than the wire-level rate
  Working with vendors to understand where the bottlenecks are

## Slide 31: Collaboration with other tasks
31

## Slide 32: Interfacing with our collaborators
Discussions with
  Task 2: Compiler
  Task 8: Chapel
  Task 11: Hardware
Chapel’s runtime interface is close to ours

## Slide 33: Chapel’s runtime interface: tasks

## Slide 34: Chapel’s runtime interface: tasks

## Slide 35: Questions around integrating with Chapel
How big is a locale?
  “Chapel native”: SMP node within cluster
  XMT: entire machine
  Locale per core?
How should latency tolerance be integrated?
  “Chapel native”: User-level domain map
  Extended types, for compiler-level code generation
  Context switch on all memory operations?

## Slide 36: Conclusions
36

## Slide 37: Conclusions and next steps
Developing benchmarks to drive runtime design
Delegate performance is no longer the bottleneck
Aggregation improves effective message rate
Work on common runtime interface is progressing
Next review period
  Multi-threaded network performance?
  Explore extended memory semantics using delegation
  Imbalanced tree benchmark on SoftXMT runtime